## Slide 1: SRON – TUD – KID analysis
Automated Analysis Routines for KID data processing

## Slide 2: Always Keep Thinking Yourself
This piece of code is always in the test phase. Hence it cannot be considered flawless. See if your results make sense. Consult an expert if you’re not sure.
Check optimum powers
Check jumping KIDs
Read the screen output (both building in and matlab warnings).
Aka, the disclaimer

## Slide 3: General Considerations
All the routines store their workspace in .mat files
Main routines return a struct containing all imported data as well as processed data. Making follow-up easier.
Why this is useful

## Slide 4: Overview
Main routines
RESPONSEanalysis
  PowerDependenceS21
Lifetime analysis (TBD, problematic)
NOISEanalysis
  NoiseCompare
  NEPcompare
ConvertS21_TUD2SRON
ConvertNoise_TUD2SRON (TBD)
Notes: K-band = NIR (2.2 um ± 195 nm)

## Slide 5: Overview
Subroutines
Blackbody
(optical experiments)
FitS21main
GenerateColorsFromMap
import_data
(general read for SRON LabView output)
legendtitle (TeX titles)
ReadSRONcsv (general read)
WriteSRONcsv (general write)
Notes: Mass mass relation

## Slide 6: TUD2SRON conversion
Functionality
Reads all S21 measurement files or Noise measurement files. Sorts them by (KID,P) and writes for each (KID,P) combination a single file containing all temperatures
Notes: Mass mass relation

## Slide 7: TUD2SRON conversion
Common errors and mistakes
The routine sorts all data to form (KID,P) pairs. Check if in input and output dir there are equal number of powers
Problems with “fopen” usually mean typo’s in input or output dir
Make sure in Delft LabView that measurement temperature is printed to file.
Noise conversion is not robust against missing files. Hence: Every S21 file, must have matching all (FFT), ON-IQ and OFF-IQ files.
Notes: Mass mass relation

## Slide 8: Response Analysis
Functionality
Read in S21 scans
Fit S21
Determine phase and amplitude responsivity by differentiation and fit
Create figures and csv output
Limitations:
Only one material and one stopoffset (avoid jumping resonators) per analysis
Notes: Mass mass relation

## Slide 9: Response Analysis
Common errors and mistakes
Warning for line 1014: Ignoring complex data is common for Khalil fits. This can be safely ignored.
Notes: Mass mass relation

## Slide 10: Power Dependence
Functionality
Load Response analysis workspace
Shows the base temperature power dependence
Limitations:
Base Temperature = min(T) as found by Response Analysis
Notes: Mass mass relation

## Slide 11: Noise Analysis
Functionality
Read in all Noise measurement files into NOISE struct
Fit S21 IQ mixer data
Calculate frequency noise (Sf/f2)
Calculate various mean noises
Determine Popt (using limited Fres shift and min ampl noise @ 100 Hz)
Fits Frequency noise @1kHz vs Pint
Generate figures
Notes: Mass mass relation

## Slide 12: Noise Analysis
Common errors and mistakes
Warning
Notes: Mass mass relation

## Slide 13: Noise Compare
Functionality
Load the Noise analysis workspace
Load Popt
Load Off resonance noise (if available)
Calculate system noise
Fit Freq noise (various F) vs Pint
Generate figures
Notes: Mass mass relation

## Slide 14: Noise Compare
Common errors and mistakes
Warning
Notes: Mass mass relation

## Slide 15: NEP compare
Functionality
Loads the workspace of Noise and Response analysis.
Loads Popt.csv and dRdtheta.csv
Calculates for min(T) and Popt the dark NEP
Create figures
Notes: Mass mass relation

## Slide 16: NEP Compare
Common errors and mistakes
Warning: This requires a dRdtheta.csv file typically made in a lifetime analysis. No standard lifetime analysis is in this package
Notes: Mass mass relation